Simulating X-ray Burst Flame Propagation: From Parallel Plane to Full Star
Zhi Chen1 and Mike Zingale1
1Department of Physics and Astronomy, Stony Brook University, Stony Brook, NY 11794-3800, USA
INTRODUCTION
PARALLEL PLANE SIMULATION RESULTS
General Info:
9216 × 1536 zones or 20 cm resolution in finest grid
R = [0, 1.843 × 105 cm] and Z = [0, 3.072 × 104 cm]
~ 3,000 GPU node hours to finish at t = 120 ms.
Shows results between two networks: aprox13 and subch_simple, they differ as subch_simple includes:
An X-ray burst (XRB) is a thermonuclear runaway caused by the ignition of the accreted fuel on the surface of a neutron star. The burst oscillation behavior observed during the rise-time of the burst and difference between the accretion and burst timescales both suggest that nuclear ignition is likely to begin in a localized region (hotspot), and spread to the rest of the neutron star. The goal is to use numerical simulations to study the XRB flame dynamics:
Study the effect of nuclear reactions on 4He flame propagation in a localized region on the rotating pole with 2D R-Z geometry.
Study the effect of variation in rotational forces on 4He flame as it spreads across the full star with 2D R-θ geometry.
{}^{12}\mathrm{C} + ^{1}\mathrm{H} \rightarrow {}^{13}\mathrm{N} + \gamma
{}^{13}\mathrm{N} + \alpha \rightarrow {}^{16}\mathrm{O} + \gamma
INITIAL MODEL
Corotating frame with consideration of rotating pseudo forces.
Assumed a 1.4 M⊙ NS with R=11 km and Ω = 1000 Hz.
Pure Helium-4 accretion layer for pure Helium XRB.
Initial model is in hydrostatic equilibrium.
Isothermal base with T = T* and pure 56Ni composition for 0 < z < H* to represent the underlying neutron star.
A transition phase with prescribed temperature and composition profiles that blend the base and atmosphere for H* < z < H* + 3δatm.
Isentropic atmosphere with pure 4He composition for z > H* + 3δatm to represent the accretion layer.
A temperature perturbation on the left part of the domain to drive a rightward propagating flame, a spreading hotspot for our geometry.
Fig: Top Panels: Time evolution of the density weighted T (left), nuclear energy generation rate (mid), and flame position (right). Bot Panels: Time evolution of total mass of 12C, 16O, and 32S.
Fig: Slice plot showing average atomic weight at t = 50 ms.
FULL STAR SIMULATION RESULTS
General Info:
1536 × 172,800 zones or 20 cm resolution in finest grid
R = [1.1 × 106 cm, 1.13072 × 106 cm], θ = [0, π]
Will need ~100,000 node hours to reach 1 s of simulation time.
Ongoing simulation!
Fig: Zoom-in of the initial temperature profile
CODE
 Castro
Microphysics
Pynucastro
| https://github.com/AMReX-Astro/Castro
| https://github.com/AMReX-Astro/Microphysics
| https://github.com/pynucastro/pynucastro
New Contributions
Are Welcome!
Fig: Strong scaling of the Full Star XRB problem.
The work at Stony Brook was supported by DOE/Office of Nuclear Physics grant DE-FG02-87ER40317.
This research was supported by the Exascale Computing Project (17-SC-20-SC), a collaborative effort of the U.S. Department of Energy Office of Science and the National Nuclear Security Administration.